# Specifications for ISC6000 &6500 Manual Clutch-Operated Roller Shades:

# PART 1 - GENERAL

  - SCOPE / DESCRIPTION

- Furnish and install manual roller shade(s) as manufactured by Sunair Awnings & Solar Screens, P.O Box 1068 Jessup, MD 20792 in accordance with the specifications below.

  - SUBMITTALS

- Product Data: Manufacturers data sheet shall be submitted for each product specified including, finishes, dimensions, options, and installation instructions.

B.  Drawings and diagrams: Product details, installation details,

working and assembly drawings shall be supplied as requested.

- Sample:  Contractor or agent shall supply samples as required.

# QUALITY ASSURANCE

A.  Product shall be manufactured to meet or exceed the quality

and standards of the SUNAIR(  product as per description

above.

B.  Supplier shall be approved to supply the products specified and

shall honor all claims and warranties as specified in accordance

with warranty.

SUNAIR( AWNINGS & SOLAR SCREENS  P.O Box 1068  Jessup, MD  20794

Phone:  410-799-1145     1-800-548-0408   Fax:  410-799-5584   www.sunairawnings.com      Info@sunairawnings.com

- Provide shades from one manufacturer for the entire project.

# DELIVERY STORAGE AND HANDLING

A.  Product shall be delivered to site in manufacturer’s original        packaging.  Product shall be labeled with product name and location of installation as indicated on Drawings.

B.  All products should be stored and handled to prevent damage to

materials, finishes, and operating mechanism.

# WARRANTY

- Manufacturer shall honor product warranty from date of   installation (See specific warranty detail available from SUNAIR( Awnings & Solar Screens).

# PART 2 – PRODUCT

# 2.1  ROLLER SHADES

# Acceptable products:  ISC6000,  ISC6500, ISC6600, and  ISC7000, as manufactured by:  East Coast:  SUNAIR( Awnings and Solar Screens (Awnings Unlimited Inc) P.O Box 1068 , 7785 Rt. 175 Jessup, MD. 20794. 800–548-0408.  West Coast:  SUNAIR( West 3803 West Thomas Rd, Phoenix AZ.  877-272-3920.

- Shade Band Material / Fabric:  Roller Shade fabric shall be inherently flame retardant, fade and stain resistant, anti-static, anti-microbial light filtering, room darkening, or “black out “ providing 0 – 15% openness factors.  The fabric shall pass NFPA 701-99 Test 1.  Bottom hem shall be ultrasonically welded with either internal or external hem bar.  Shades that have railroaded fabric may have horizontal heat welded seams.  Fabric will be selected by architect from the SUNAIR standard fabric collection.

- Tubing:  The roller tube will range between 1 ½” to 3” to be compatible with selected range sizes.  The tubing shall be manufactured from 6063 T5 aluminum with sufficient thickness to prevent excessive deflection.

- Direction of Roll:  back of roller is regular, reverse roll is available and can be specified

SUNAIR( AWNINGS & SOLAR SCREENS  P.O Box 1068  Jessup, MD  20794

Phone:  410-799-1145     1-800-548-0408   Fax:  410-799-5584   www.sunairawnings.com      Info@sunairawnings.com

- Bottom / Hem bar: To be extruded aluminum either; Standard bottom bar with internal extruded aluminum bar with sealed ends or optional external bottom bar extruded and powder coated color to match hardware brackets and accessories.

- Mounting brackets:  Shall be steel powder coated to match hardware and allow removal of the roller tube assembly without removing the brackets.

- Shade operation:  Manual; with continuous loop beaded chain #10 nickel plated steel.  Optional stainless chain can be specified.  Clutch shall have the capacity to lift the size and weight of the shade.  Spring “assist” will be specified for all shades larger enough to require the device.   Cord tensioning safety device shall be installed with all shades.

- Limit stops: Upper and lower stop balls provided to prevent damage to shade fabric.

- Chain Length: Full length of shade standard, custom lengths available.

- Option: Crank operated mechanism with gearbox drive system controlled by crank handle. Handle length is manufacturer’s standard.

- Option: Spring operated shade with positive locking mechanism that can stop shade movement at half-turn of roller with standard pull.

- Any substitutions must be submitted for approval 30 days prior to close of bid.

  - ROLLER SHADE FABRICATION

A.  Field measure and verify sizes prior to manufacturing after all

other work has been completed. Clearances for operating hardware of operable glazed units will be noted.

- Ensure that the shade fits from top to bottom of window and that the edge of the bracket is no more than ¼” from the face of the jambs.

  - ACCESSORIES

  - Dual Roller Shades:  Universal mount steel brackets with 2 separate rollers working independently from each other (Solar shade and room darkening black out).

SUNAIR( AWNINGS & SOLAR SCREENS  P.O Box 1068  Jessup, MD  20794

Phone:  410-799-1145     1-800-548-0408   Fax:  410-799-5584   www.sunairawnings.com      Info@sunairawnings.com

  - Bottom Bar / Hem Bar:  Either Standard hem / bottom bar with internal extruded aluminum bar with sealed ends, or optional external bottom bar extruded and powder coated color to match hardware brackets and accessories.

  - Fascia:  L shaped removable aluminum extrusion valance that attaches to the brackets and conceals the roller tube.  Color will match other hardware and will be powder coated. 3” and 4” fascia as specified on all shades up to 108” in length, and 4” fascia as specified on all shades greater than 108” in length.  Standard flat /square fascia or optional rounded fascia. 7” fascia as is specified on Duo shades ISC6500 & ISC6600.

  - Black out tracks as specified on room darkening and black out shades.  Powder coated aluminum to match hardware color.  Color and finish as selected from manufacturer’s full range.

  - Cassette 3” and 4” to enclose standard shade roller, as specified on ISC6000  and ISC7000 shades.

# PART 3 –EXECUTION

# INSTALLATION

A.  Install shades level and plumb, and align with adjacent units

if necessary.

- Adjust roller shade to operate smoothly

  - DEMONSTRATION

A.  Demonstrate operational method and instruct owner’s personnel

in proper operation and maintenance of the shade.

END OF SECTION

SUNAIR( AWNINGS & SOLAR SCREENS  P.O Box 1068  Jessup, MD  20794

Phone:  410-799-1145     1-800-548-0408   Fax:  410-799-5584   www.sunairawnings.com      Info@sunairawnings.com

# Text boxes

Revised 4/8/13

SPECIFICATION

Section 12492   ISC6000 - 6500  Manual Roller Shades

Division 12

P.O. Box 1068  7785 Rt. 175,

Jessup, MD 20794

JESSUP, MD       800 – 548 – 0408

PHOENIX, AZ      877 – 272 - 3920