# Specifications for SUNAIR® Retractable Lateral Arm awnings:

# PART 1 - GENERAL

  - SCOPE / DESCRIPTION

- Furnish and install retractable lateral arm awning(s) type as

manufactured by Sunair Awnings & Solar screens , P.O Box 1068

Jessup, MD 20794 in accordance with the specifications below.

  - SUBMITTALS

- Product Data: Manufacturers data sheet shall be submitted for  each product specified including finishes, dimensions, options and installation instructions.

B.  Drawings and diagrams : Product details, installation details,

working and assembly drawings shall be supplied as requested.

- Sample:  Contractor or agent shall supply samples as required.

# QUALITY ASSURANCE

A.  Product shall be manufactured to meet or exceed the quality

and standards of the Sunair awning as per description above.

B.  Supplier shall be approved to supply the products specified and

shall honor all claims and warranties as specified in accordance

with warranty.

SUNAIR AWNINGS & SOLAR SCREENS  P.O Box 1068  Jessup, MD  20794

Phone:  410-799-1145     1-800-548-0408   Fax:  410-799-5584   www.sunairawnings.com      Info@sunairawnings.com

- Provide awnings from one manufacturer for the entire project.

# DELIVERY STORAGE AND HANDLING

A.  Product shall be delivered to site in manufacturer original

packaging.

B.  All products should be stored and handled to prevent damage to

materials, finishes, and operating mechanism.

# WARRANTY

- Manufacturer shall honor product warranty from date of   installation (See specific warranty detail available from Sunair Awnings & Solar Screens).

# PART 2 – PRODUCT

# 2.1  AWNING

# Acceptable manufacturer:  East Coast:  Sunair Awnings and Solar Screens (Awnings Unlimited Inc) P.O Box 1068, 7785 Rt. 175, Jessup, MD 20794. 800–548-0408.  West Coast:  Sunair West 3803 West Thomas Rd, Phoenix AZ 877-272-3920.

- Any substitutions must be approved 30 days before close of bid.

- Arm elbow and shoulder components shall be made of forged aluminum 6061-T6.

- Arm cables shall be stainless double cable design 5/32nd   mill spec DTL83420.

- All arms 10’ 2” and above in projection shall have each three (3) internal steel springs.  6’ 11” and 8’ 7” arms shall have two (2) internal springs in each arm.

- Roller tube, Support Tube, and Front bar shall be extruded aluminum 6005 T5 or 6161-T6.

- All nuts and bolts shall be stainless steel.

- Hoods shall be “one piece” extruded, powder coated aluminum to match the frame color and end caps to match.

SUNAIR AWNINGS & SOLAR SCREENS  P.O Box 1068  Jessup, MD  20794

Phone:  410-799-1145     1-800-548-0408   Fax:  410-799-5584   www.sunairawnings.com      Info@sunairawnings.com

  - AWNING FABRICATION

A.  Product Description:  Awning assembly shall include 10” extra

fabric on the roller to cover the aluminum tube when the awning

is fully extended.

- Unit Size:  Field measure each awning.  Verify applicable size for the application.

C.   AU10 wall brackets will be used on standard wall installations.

AU16 ceiling brackets for ceiling mount installations.

Additional AU18 roof brackets shall also be used for roof mount

installations.

  - Motorized Awnings

A.  Motors and controls shall be manufactured by Somfy Inc. in

Cranberry New Jersey from their standard available range.

# PART 3 –EXECUTION

# INSTALLATION

A.  Install awnings level and plumb, set the pitch even, and as

appropriate.  Adjust  arms if necessary.

- Install brackets according to the manufacturers’ recommended installation methods.

- If motorized, set the limit switches and program all remotes.  Wire all motors to local codes

  - DEMONSTRATION

A.  Demonstrate operational method and instruct owner’s personnel

in proper operation and maintenance of the awning.

END OF SECTION

SUNAIR AWNINGS & SOLAR SCREENS  P.O Box 1068  Jessup, MD  20794

Phone:  410-799-1145     1-800-548-0408   Fax:  410-799-5584   www.sunairawnings.com      Info@sunairawnings.com

# Text boxes

SPECIFICATION 10536   AWNINGS

Sunair Retractable Lateral Arm Awning

Division 10

Revised 1/30/13

P.O. Box 1068  7785 Rt. 175,

Jessup, MD 20794

JESSUP, MD       800 – 548 – 0408

PHOENIX, AZ      877 – 272 - 3920